## Slide 1: Humber Bridge Review Results from the HUMBER ESTUARY TRANSPORT MODEL
Notes: 2
2
2

## Slide 2: This presentation
The model
Results of option tests
  Traffic impacts
  Economic appraisal

## Slide 3: Purpose of the model
To allow the assessment of the impact of different tolling scenarios for the Humber Bridge on both:
  traffic flows
  the Humber area economy
Designed to be consistent with the DfT’s Transport Analysis Guidance (WebTAG)
Designed to forecast the demand response to changes in the tolls in terms of the number & destination of trips made, as well as route choice

## Slide 4: Model area
Full extent: area bounded by Thirsk, Scarborough, Grantham, Boston.
Western boundary: A1
>200 traffic origin/ destination zones plus externals

## Slide 5: Model area
Network where all traffic movement actively simulated (links and junctions shown):
west of Scunthorpe to east of Hull
150 traffic O/D zones

## Slide 6: Model capability
3 time periods: am peak, interpeak, pm peak
5 vehicle types: private car, 4x goods vehicle classes
5 passenger journey purposes:
  home-based: journey to work, employer’s business, other
  non home-based: employer’s business, other
3 income classes (low, medium, high) for commuting & other
  each has its own demand elasticity w/ respect to trip cost
3 model years: 2010, 2021, 2033
Does not model public transport

## Slide 7: Model source data
Update & extension of pre-existing north bank model
41,000 roadside interviews on trip origin/destination, journey purpose at 38 sites (5,000 interviews at 5 sites bespoke for this study);
>100 traffic count sites
Growth in trips 2010-2033 from DfT National Trip End Model (NTEM) forecast, version 6.2 incorporating the effects of the 2008/09 recession

## Slide 8: Toll option tests
Base case (Do Nothing) = existing toll level in real terms (£2.70 per car in 2010 prices)
Toll levels tested:
  No toll
  Maintenance-only level toll, £1 per car (63% reduction, other vehicle classes pro rata)
  £2 per car toll (26% reduction)
  £2.43 per car toll (10% reduction)

## Slide 9: Traffic in the base model (2010)

## Slide 10: Bridge traffic northbound, am peak

## Slide 11: Bridge traffic southbound, am peak

## Slide 12: Base case, growth in traffic 2010-2033

## Slide 13: Base case, growth in congestion delays 2010-2033

## Slide 14: Traffic impact of removing tolls (2010)

## Slide 15: Impact of reducing tolls by 63%

## Slide 16: Impact of reducing tolls by 10%

## Slide 17: Change in congestion delays in zero tolls option (2033 am peak)

## Slide 18: Modelled effect of toll level on traffic

## Slide 19: Modelled effect of toll level on traffic

## Slide 20: Effect of toll level on traffic, base year (with full demand response)
Toll at 2010 prices | Change in toll | Change in traffic am peak |  | Change in traffic interpeak | 
2.70 |  | Humber Bg | M62 Goole | Humber Bg | M62 Goole
2.43 | -10% | 3% | 0% | 3% | 0%
2.00 | -26% | 10% | -1% | 10% | -1%
1.35 | -50% | 25% | -1% | 26% | -1%
1.00 | -63% | 32% | -2% | 35% | -1%
0.00 | -100% | 54% | -2% | 67% | -5%

## Slide 21: Economic appraisal
Economic efficiency of the transport system analysis:
  For commuters, other consumers, businesses (passenger and road freight), impact on:
    travel time
    vehicle operating cost
    user charges
  For the public sector, direct revenues and indirect tax revenues

## Slide 22: Economic appraisal
Wider impacts analysis:
  Agglomeration benefits
  Welfare benefits
Broadly speaking, the benefits to employers and employees of a broader, deeper labour pool in a sub-regional labour market

## Slide 23: Economic appraisal – transport economic efficiency

## Slide 24: Economic appraisal – transport economic efficiency

## Slide 25: Economic appraisal – transport economic efficiency

## Slide 26: Present value of benefits and costs before wider impacts

## Slide 27: Present value of benefits and costs before wider impacts

## Slide 28: Present value of benefits and costs with wider impacts

## Slide 29: BCR by toll level